## Slide 1: Overview of Onsite Sewage Treatment and Disposal Systems
Bureau of Environmental Health
Division of Disease Control and Health Protection
Florida Department of Health
August 1, 2019

## Slide 2: What is an OSTDS?
Onsite sewage treatment and disposal system
Includes septic systems (septic tank and drainfield) but also includes systems capable of greater treatment

## Slide 3: Septic Systems and “Advanced” Systems
Septic tanks provides basic treatment
  Removal of solids and fats, oils and greases
“Advanced” systems provide greater treatment
  Removal of degradable organic material
  Removal of nutrients

## Slide 4
OSTDS are among the many sources contributing nitrogen to groundwater.
OSTDS are recognized as low-cost and long-term approaches to wastewater treatment
Are effective and protective when properly designed, installed, operated, and maintained
EPA/625/R-00/008 February 2002
Office of Water Office of Research and Development U.S. Environmental Protection Agency
Onsite Wastewater Treatment Systems Manual

## Slide 5: Modern OSTDS in Florida protect Public Health and the Environment
About 2.4 million OSTDS serve a third of the state
OSTDS are effective alternative to central sewer
  Less environmentally disruptive in some areas
  Less than 40% of OSTDS in environmentally sensitive areas
Construction standards and setback distances protective
  Primarily protect public from waterborne illness
  More than 90% of drinking water in FL comes from groundwater
  The drainfield further breaks down viruses/pathogens from septic tank; can reduce nitrogen by 10-50%
Florida can and does establish policies for additional protection of sensitive environmental areas

## Slide 6: Septic Tank and Drainfield (A Conventional OSTDS)
http://www.epa.gov/owm/septic/pubs/homeowner_guide_long.pdf
18

## Slide 7: How Do Septic Tanks Work?
Modern septic tanks are water tight
Collect solids and consume a third to half of biodegradable material (carbonaceous biochemical oxygen demand after 5 days[CBOD5])

## Slide 8
Groundwater
Liquid that comes from septic tank drains into soil
Soil/Air/Water combination:
  Removes/filters pathogens, suspended solids in the area above groundwater
  Converts ammonia to nitrate (removes 10-50% of nitrogen)
How Does a Drainfield Work?

## Slide 9
2 feet between bottom of drainfield and wet season water table required to provide air and soil treatment
6 inch between top of drainfield and ground surface
Drainfield thickness (12 inch for gravel)
Modern Drainfield Design Protects the Environment
Separation to wet season water table important for treatment

## Slide 10: Mound As Alternative Drainfield
A system can be elevated (Mound system) to protect environment
• Wet season water table too high
• Prohibited soils (e.g., rock) exist

## Slide 11
To limit OSTDS-contribution of nutrients (in general or for specific areas)
  Lower the number of OSTDS
    Sewer
    County ordinances (lot size, setback)
    Existing statute density-limitations (Sections 381.0065(4)(a)-(g), Florida Statutes)
  Require higher treatment by OSTDS
Options for Nutrient Reduction

## Slide 12: Aerobic Treatment Unit (ATU)
Aeration
Tank or Compt.
Sewage
Pretreatment Tank or Compartment
Drainfield
Clarifier
ATU certification based on certain performance standard
All ATUs certified to meet standard NSF 40; some are also certified to meet a 50% nitrogen-reduction standard (NSF 245)

## Slide 13: Performance-Based Treatment System (PBTS)
Specialized onsite sewage treatment and disposal system
In many cases, includes an ATU
Designed and certified by professional engineer to achieve specific and measurable established performance standards for:
Carbonaceous biochemical oxygen demand,
Total suspended solids,
Total nitrogen,
Total phosphorus,
Fecal coliforms

## Slide 14
PBTS Based on Nitrogen-Reducing ATU
Aeration
Chamber
recycle for denitrification
Sewage
Drainfield
One example of a nitrogen-reducing ATU
Field evaluations show about 50% nitrogen reduction
More complex technologies with higher treatment effectiveness are becoming available

## Slide 15: Two-Stage Nitrogen Reduction Process Example
Note: In flat landscapes may need a single pump.
Septic Tank
Pretreatment
Stage 1 Biofilter
Nitrification
Stage 2 Biofilter
Denitrification
Drainfield
Ground Surface
Wastewater
Q
In-tank Nitrogen Reduction Biofilter - PBTS

## Slide 16: In-ground Nitrogen-Reducing Biofilter
A nitrate-reducing layer below drainfield; material reacts with nitrate

## Slide 17
Dr. Kendra Goff - Chief
Kendra.Goff@flhealth.gov
(850) 245 4250
Ed Barranco- Section Lead Dr. Eb Roeder
Ed.Barranco@flhealth.gov Eberhard.Roeder@flhealth.gov
Dr. Xueqing Gao Debby Tipton
Xueqing.Gao@flhealth.gov Debby.Tipton@flhealth.gov
Onsite Sewage Programs Section
Bureau of Environmental Health
Division of Disease Control and Health Protection