## Slide 1: eAOR Training
Division of Air Resource Management (DARM)
Compliance Assurance Section
January 2026

## Slide 2: Overview
  Annual Operating Report (AOR)
    Regulatory Requirements
    Submittal Procedures
  Electronic AOR (eAOR) Updates/Important Info
  Signature and eAOR Submission Requirements
  PIN Requests
  Emissions Fees (Title V sources only)
  Data Review and Calculation Tips
  eAOR Demo
  Contacts

## Slide 3: AOR Requirements
  In accordance with Rule 62-210.370 (3), F.A.C., the following facilities shall submit an AOR to DEP each calendar year for which the facility operated and/or had an active permit:
    All Title V Sources;
    All synthetic non-Title V sources;
    All facilities with the potential to emit ten (10) tons per year or more of volatile organic compounds or twenty-five (25) tons per year or more of nitrogen oxides and located in an ozone nonattainment area or ozone air quality maintenance area; or
    All facilities for which an annual operating report is required by rule or permit.
    AOR Form with instructions: DEP Form 62-210.900(5)
    Due by April 1st of the following year.
    Visit DEP’s AOR webpage for more information.
Notes: EPA’s Air Emissions Reporting Rule (https://www.epa.gov/air-emissions-inventories/air-emissions-reporting-requirements-aerr) and our AOR rule requires us to compile and update emissions inventories. These inventories are used for many things including: national trend assessments and modeling activities to help develop emissions standards, regulations and policies, identify at risk populations, assess air pollution control efficiency, and to set permit requirements and determine compliance with emissions limits. It’s also used by our Department to assess emissions fees required for Title V facilities, which helps fund our air permitting and compliance programs.
If your facility is classified as a Title V major or synthetic minor source, has potential to emit above certain regulated pollutant thresholds, or has a requirement in the permit, you must complete an AOR for each calendar year it’s in operation and/or has an active operating permit in accordance with 62-210.370(3), Florida Administrative Code (F.A.C.).
The Department sends out AOR reminder letters in December to facilities that have a status of Active or Construction in our database. It’s also sent to some inactive facilities if the final shutdown occurred during the reporting year.
  For facilities that are still under construction status and did not begin operations during 2025 but got an AOR letter, just let us know so we can mark you off the list of facilities requiring an AOR.
  For active facilities (or EUs) that are in long term reserve shutdown and didn’t operate at all during the year, you must still submit an AOR and just indicate that you didn’t operate the facility or EU.
  For inactive facilities that did operate some during the year, you still need to submit an AOR and include emissions information for the portion of the year you operated.
The Department adopted DEP form 62-210.900(5) for submitting AORs, which can be accessed from our website.
The form includes general instructions and an Appendix (Appendix A) which provides a list of regulated pollutants and thresholds for which annual emissions must be reported. Hazardous air pollutants only need to be reported every three years. The next reporting year will be 2027. However, it’s still encouraged to provide the data as it’s beneficial and it’s not overly burdensome to report since you have to keep track of it anyways for compliance purposes.
AORs are due to be submitted to the Department by April 1st. It’s a violation if the AOR is submitted late and penalties are assessed if Title V fee payments are late (to be discussed later).

## Slide 4: AOR Submittal Process
  There are two ways to submit for non-Title V sources.
    Mail or email a completed/signed PDF copy of the AOR Form to the appropriate DEP District or approved Local Air Program.
    Submit electronically using DEP’s eAOR system.
      (If submitted via eAOR, there is no requirement to mail/email it to the DEP or Local Air Program office.)
  Title V facilities are required to use eAOR unless a technical or financial hardship is claimed.
    If you need to claim a hardship from using the eAOR system, please contact the AOR Coordinator at EAOR@FloridaDEP.gov.
    Note: Please be aware that DEP can no longer provide partially pre-filled PDF AOR forms.
Notes: For non-title V facilities, you have two options for submitting your AOR.
  Mail or email a completed and signed PDF Form to your compliance authority whether that be a DEP district or one of the approved local air programs as indicated on the air permit. Contact information for these offices can found on these links.
  Your second option is to use eAOR to submit it electronically. If you do this, there is no need to send the form to your compliance office.
For TV facilities, you are required by rule to use eAOR unless you claim a technical or financial hardship. Please contact the AOR Coordinator at EAOR@FloridaDEP.gov if you need to claim a hardship from using the eAOR system.
If you are mailing in a form, make sure it’s postmarked by April 1st.
Note: Please be aware that DEP can no longer provide partially pre-filled AOR forms. DEP has replaced the old eAOR software with an online system, which does not retain this feature. However, the new system does resolve many of the challenges that has deterred people in the past from using eAOR. The new system is more user friendly and has many benefits (see AOR Webpage) that make completing and submitting an AOR easier. Therefore, we strongly encourage non-Title V sources to use the new eAOR system system.

## Slide 5: eAOR System Update
  The Department has replaced the antiquated eAOR software with a new online system for submitting electronic AORs.
  Old software no longer supported.
  Same fields as old system, but interface is more user friendly.
  Also prefills much of the facility data, displays last year’s AOR data for reference, has a calculation worksheet, has help and data verification features, automatically calculates TV fees, etc., like the old system.
  Plus has a few new “convenience” features.
Notes: The Department has replaced its eAOR software with a new online system, which eliminates many of the previous obstacles users faced with installing the antiquated software on their computers.
The old eAOR software is no longer supported and can no longer be used to access facility data or submit AORs.
The new system has basically the same structure and fields, but with a interface that is more user friendly.
Like the old system, the new eAOR:
  prefills some much of the facility information into the form;
  allows for comparing your data to what was submitted the previous year;
  has help and data verification features;
  allows you to set up calculation formulas that can be reused on future submissions;
  saves completed submissions to PDF;
  automatically calculates TV fees; and
  allows for signing/submitting the AOR electronically so you don’t have to worry about mailing it to the correct office.
The new system also has a few new “convenience” features. For example, you can now add contributors to your AOR so more than one person can work on it if necessary. There is a contact import and copy function so you don’t have to type in contact info if they are the same for owner/RO, facility contact, or report contact. And there is a new feature that allows you to send a notification email to the owner/AR or once the AOR is ready to be signed/submitted.

## Slide 6: Bugs and Enhancements
  New system may still have bugs.
    Since the system is new, it is very important that facilities start working on their AORs as soon as possible this coming year as there may be system bugs encountered that could delay submittals.
    Any eAOR system issues encountered should be reported immediately to: DARM.Helpdesk@FloridaDEP.gov.
    Please put “eAOR Bug” along with your facility ID in the subject line of the email and include as much detail as possible regarding the issue you’re seeing.
  Enhancements to improve the system will be ongoing. Feel free to send us suggestions!
Notes: We are still working on some known bugs, but they are minor and able to work around. For example, the Control Equipment dropdown fields on the pollutant edit screen only displays a code and not the description. See Assistance on AOR webpage for a link to the codes with descriptions. There is also an issue with the Import feature on the calculation sheet.
There could be issues we did not catch doing our beta testing of the new system as it can be difficult to test every scenario.
If you come across an issue that prevents you from completing an entry, please email us asap and include as much detail as possible regarding the issue you’re seeing. Screenshots are a plus!
There should not be any issues to prevent you from submitting, but we strongly recommend you start on your AORs as soon as possible just in case you come across an issue that could delay submittal.
Enhancements – These won’t be done for this year because we’ll be focusing on fixing bugs, but we will be continuously working to improve the system over time. If you think of anything while working in the new system that will streamline the data entry and submittal process, please send us your suggestions.

## Slide 7: How to Access eAOR
  The new eAOR system will be released and available to facility users on January 23, 2026, via the DEP Business Portal.
  To access eAOR, users will be required to have a DEP Portal account*.
  From the Business Portal homepage, follow these steps to access the system:
    Select Submit
    Select Annual Report
    Select Air Electronic Annual Operating Report
  *If you do not have a DEP Portal account, you will need to create one by clicking on “Register” from the DEP Business Portal sign-in page and filling out the required information. Once you register, a verification email will be sent to your email address with a link. Use this link to create a password for your login.
  If you need assistance with creating a Business Portal account or resetting a password, please contact the IT Service Desk at 850-245-7555 or ServiceDesk@FloridaDEP.gov.

## Slide 8: eAOR Home Page
This is where you can start a new AOR and view the list of any AORs you’ve already started.
List includes columns with info about the facility and AOR that can be filtered and sorted.
Action items (will vary depending on role – see next slide for more details on User roles):
  For In Progress AORs – continue working on your AOR, add a contributor, or delete it.
  For Submitted AORs – view the submitted AOR, print a copy of it, view the TV fee invoice (if applicable), or revise the AOR.
  Note that once an AOR has been submitted, it cannot be deleted so you won’t see that action item. You can only view or revise it that that point.
See the eAOR Facility User Guide for detailed instructions on navigating the new system.
Notes: Once you select eAOR from the Portal menu, it will take you to your eAOR Facility home page where you can start a new AOR or view the list of AORs already started or completed.
On this list there are columns for facility ID/Owner/Site Name, AOR year, submittal #, created date, submittal status and submittal date (if applicable) that can be filtered and sorted.
Action items on the right side allow you to continue working on an In Progress AOR, add a contributor, or delete it. Once it’s been submitted, the action items change to allow for viewing the submitted AOR, printing a copy of it, viewing the TV fee invoice (if applicable), or revising the AOR. Once it’s been submitted, it cannot be deleted so you won’t see that action item. You can only revise it that that point.

## Slide 9: eAOR User Roles
  AOR Manager
    Single role that defaults to the person who started the AOR.
    Able to edit the AOR.
    Only role able to delete the AOR, assign/unassign Contributors, or assign a new AOR Manager.
  Contributor
    AOR can have multiple Contributors assigned.
    Must be assigned by the AOR Manager.
    Able to edit the AOR and view existing Contributors.
  Signee
    Single role that is automatically assigned to the Owner/Authorized Representative or Responsible Official entered on the AOR.
    Able to edit the AOR and view existing Contributors.
    Only role able to sign/submit the AOR (must have a PIN).
    In some cases, the Signee may also be the AOR Manager OR a Contributor. If so, their Role will be displayed as AOR Manager, Signee OR Contributor, Signee, respectively.

## Slide 10: Signature Requirements
  For Non-Title V facilities – The Owner or Authorized Representative (AR) must sign.
  For Title V facilities – The Title V Responsible Official (RO) must sign. That may be the primary or additional RO (if one is designated). The RO signing an AOR for a Title V facility must be identified on a current Responsible Official Notification Form, DEP Form No. 62-213.202(1) on file with the Department.
  New eAOR Signature & Submission Requirement –
    In the new system, signatures must be done by the applicable Owner/AR or RO listed on the form using their PIN at the time of submission.
    Unlike before, there is no longer the option for Owners/ARs or ROs to e-sign or send a hard copy signature page separately after the AOR has been submitted by the preparer.
Notes: The person completing the AOR may not necessarily be the person responsible for signing it. Many facilities may have a person or consultant who completes the AOR, but it’s the Owner/Authorized Representative that must sign for non-TV facilities and for TV facilities, it must be the Responsible Official (primary or alternate if one is designated on the appropriate RO form).
The RO signing an AOR for a Title V facility must be identified on a current Responsible Official Notification Form, DEP Form No. 62-213.202(1) on file with the Department.
Please be aware that the signature and submittal process in the new eAOR is different from the old process.
Anyone with a Business Portal account can start and work on an AOR in the new eAOR system, but it can only be submitted by the applicable Owner/Authorized Representative or Responsible Official by using their PIN to sign electronically.
In the old eAOR software, the AOR could be submitted by another party preparing the report and a signature (either an e-signature or hard copy signature page) submitted separately. This is no longer the case as the e-signature via PIN is required to submit the report in eAOR.

## Slide 11: eAOR Submissions
  While anyone who has a Business Portal account can start and work on an AOR, it can only be submitted by the Owner/AR or RO listed on the AOR by using their PIN to sign electronically.
  The Owner/AR or RO is automatically assigned to the Signee role once their information is entered and saved on the AOR.
  New eAOR feature lets a report preparer send an email to the Owner/AR or RO once the report is ready to be signed/submitted.
Important Note: If your company plans to have more than one person working on the same AOR, please carefully coordinate with your team on who will start the AOR. If more than one person starts the same AOR and enters the Owner/AR or RO (the Signee), that AOR will show on the Signee’s Home Page as two separate In Progress AORs. If the Signee sees this, they might be confused as to which one to sign. So, make sure only one person is starting the AOR, but also advise your Signee that if they see multiple versions to check with the AOR Manager(s) to ensure they are signing the correct AOR.

## Slide 12: PIN Requests
  For Owners/Authorized Representatives or Responsible Officials needing to obtain a PIN to electronically sign/submit AORs, please be aware this process has also changed and may take longer than before as it involves more steps.
  It is very important that anyone who needs to obtain a PIN starts the process as soon as possible rather than wait closer to the deadline for submitting the AOR.
  This process is now done in our DEP Business Portal. If you do not have an existing Portal account, you will need to register and sign in under your account to initiate a PIN request.
  Instructions for requesting a PIN can be found in the DEP Business Portal Guide.
  If you need assistance with PIN requests, please contact the IT Service Desk at 850-245-7555 or ServiceDesk@FloridaDEP.gov.
Notes: This process has also changed! DARM no longer handles PIN requests. It’s done by our IT Section via the Business Portal.
If you have an old PIN that was issued by DARM, it will not work in the Portal. You will need to obtain a new one through the Business Portal.
The new process is also a little more involved and may require more time as the PIN application must be signed, notarized, and mailed to DEP’s Tallahassee office.
Do not delay on getting a PIN! It’s the only way to submit your AOR in eAOR.
If you have questions or need assistance with PIN requests, you’ll have to contact our IT Service Desk as DARM does not handle this process anymore.

## Slide 13: Title V Emissions Fees
  Fees are calculated based on emissions reported for “marked” pollutants.
    Marked pollutants are regulated pollutants that have a numerical emissions limit or emissions cap in the permit and are display in eAOR with an asterisk next to them (for example *PM).
  Upon submission in eAOR, a Title V fee invoice is generated.
  Fee payments are also due April 1st.
    A penalty of 50% of the amount of the unpaid fee, along with interest fees pursuant to Section 55.03(1), Florida Statutes, is assessed on late payments.
  Two methods of payment are available.
    If paying by check, send the invoice and check by regular or certified mail to the below address and make the check payable to the Florida Department of Environmental Protection.
    Title V Emissions Fee Coordinator
    Division of Air Resource Management
    2600 Blair Stone Road, MS 5500
    Tallahassee, FL 32399
    If paying by electronic transfer of funds, please contact Amy Hilliard at 850-717-9025 for wiring instructions or email us at EAOR@FloridaDEP.gov.
  More information can be found at: https://floridadep.gov/air/permitting-compliance/content/title-v-fees
Notes: If mailing a check, it must be posted marked by April 1st, or it will be considered late and subject to penalties and interest.
It’s also important to include the invoice with the check or we may not be able to process the check.
If doing a wire transfer, please contact Amy Hilliary for instructions. Do not use the link from instructions sent last year as it changes each year.
DEP is in the process of implementing an online payment feature in the Business Portal for Title V fees. We are not sure if it will be available for this AOR season. As soon as it’s available, the Title V fee webpage will be updated with instructions.

## Slide 14: Data Review
  After starting your AOR, please remember to review your prefilled data before completing the report.
  If there is an error in the prefilled data, for example, a pollutant has an emissions limit in the permit but is not ‘marked’ in eAOR (*), or an emissions unit is missing, please contact us before starting your eAOR data entry.
  If you need to invalidate or add an SCC in eAOR and are unsure of what to do or which SCC to use, please first check with us.
  Remember the RICE – Emergency / Limited Use/Black Start Engines that have numerical emissions limits for any pollutant or meet the threshold are to be included in AORs.
Notes: Don’t forget to review your data for accuracy! Sometimes there may be delays in updating data in our database so it’s important to verify it on your end.
One of the most important things for TV sources to check, because it affects fee calculations, is the accuracy of marked pollutants. Ensure that all pollutants with an emission limit in the permit are marked with an asterisk in eAOR. (This includes a % sulfur limit on fuels.)
If you see any inaccurate data or need to invalidate or add any SCCs and have questions about which SCC to use, please contact us for assistance.

## Slide 15: Emissions Calculations Tips
  Make sure the correct SCCs are reported in eAOR. If you are adding (or invalidating) an SCC in eAOR, and there is any question regarding which SCC to use, then please check with us first.
  Make sure the correct Emissions Method Codes used to calculate emissions are reported.
    See Rule 62-210.370, F.A.C., for methods to be used when computing actual emissions.
  Make sure to use the correct Emission Factor (EF) for the particular pollutant.
    For PM, PM10, and PM2.5 emissions, EFs used were often for the wrong pollutant. For example, AP42/Webfire EF for PM was used to report PM10.
    Depending on the SCC and control equipment configuration, there may be emission factors for *primary PM, primary PM10, primary PM2.5, filterable PM, filterable PM10, filterable PM2.5 and condensable PM (CPM).
    NOTE: ‘primary PM’ is not reported. Rather, PM determined by standard EPA Method 5 is filterable PM, which is reported.
Notes: SCC – SCC emissions factors are developed from testing for specific processes, and the SCC used in EAOR should reflect the specific process or activity that emits the air pollutant, as much as possible. For example, if the permit changed because a specific fuel is no longer allowed to be burned, then the SCC for that fuel should not be available in EAOR. Also, when gap filling HAP emissions, EPA bases it on the SCC code, so please make sure the right one is used for reporting your emissions.
Emissions Method Codes – Please make sure the highest ranked applicable emissions method listed in the rule are used for computing actual emissions. In addition, the methods used may change over time, please remember to update EAOR accordingly, including calculation sheets and emissions comments when necessary.

## Slide 16: Emissions Calculations Tips
  Make sure emission factors have the correct units.
  Provide the source of the emission factor in eAOR.
    If emissions were calculated using an emission factor based on site specific data such as stack tests, then list the test dates, and EF units; or if the EF was established in a permit, then reference which permit.
  Double check your emissions calculation formula.
    A minor omission could result in either underreporting emissions or over reporting emissions.
  CPM, PM2.5, and PM10 should typically be reported for combustion sources.
    If the information is available and the reporting threshold of 5 tons/year was exceeded (or CPM is a marked pollutant), then report the emissions. At the following link a tool is available to help estimate CPM emissions for some SCC: CPM Reporting Threshold, and Estimated Annual CPM Emissions Calculator for some SCCs.
Notes: When QA’ing the emissions data for suspect values, typically what we find is that it relates to the emissions method or emissions factor used, sometimes causing emissions to be over estimated or underreported, (or appear to be incorrect and require follow-up). The following are examples of common data quality issues I find, and what led to the issue:
A change during the reporting year in the facility’s tracking/reporting methodology resulted in underreporting of emissions: In this case, the facility went from using AP-42 emissions factor to using CEMS, however programming of the CEMS to switch to calculating the mass value was only available for part of the year, and emissions for the other half of the year not picked up by CEMS were inadvertently excluded (and subsequently had to be calculated based on the fuel consumed during this time using AP-42 emissions factors);
Different emissions factors are used for reporting in different systems (i.e. TRI vs. AOR comparison): AOR reporting schedule may precede TRI reporting, and in some cases, the more accurate emissions factors used for TRI, which considered specific controls, were not available until after the AOR reporting deadline (or were only utilized in TRI, and not EAOR) and consequently a comparison of emissions from the two systems showed a large disparity.
Observed a sig decrease in their NOx emissions in the current reporting year vs. previous year, which seemed out of proportion to process rate inc in current year (i.e. Nox CEMs, and NOX had decreased by 30%, in spite of a slight increase in the tons of coal burned). In this case, after follow-up with the facility, it was determined default CEMS values required to be used in the previous year overestimated actual Nox emissions for that year. Tip: When possible, add a note in EAOR explaining why the Nox emissions were higher in the previous year, compared to the current year.
Instances where the emissions factor or fuel usage/ process rate is off by an order of magnitude; or simply, not the right value was used in the formula in EAOR; or
The exact same process rate was reported for different fuels burned, for example diesel and natural gas.
Instances where materials or substances used in the previous year’s processes were discontinued prior to the current reporting year, however were inadvertently reported anyway;
Cases where the pollutant reported was actually not contained in any of the MSDS (in this case, emissions for chromium trioxide & titanium dioxide ‘CrO3/TiO2’ were tracked in the same column on their spreadsheet)
Cases where emissions were normally calculated by applying a control efficiency, however were inadvertently reported without it, resulting in over reporting of emissions;
Emissions value reported was in pounds because the conversion to tons was excluded from the formula;
Cases where HAP VOCs are not included with the VOC emissions; and
Cases where the workbook setup to capture data for the AOR such as fuel usage, needed the formulas to be revised; or the formula omits a conversion factor (i.e. for conversion of sulfur to SO2), underreporting emissions by half;
Spreadsheet cell containing the percent coal ash value incorrectly used a “percentage” Format type (i.e. 10% ash) instead of a “number” Format type (i.e. 0.1 ash fraction), as a result HAPS metal emissions were over reported.
Regarding Emissions Calculations, these are required to be provided in EAOR (using worksheet or attached) and should clearly show soot blowing, startup / shutdown, control eff. / capture efficiency, and fugitive emissions as applicable. If emissions are determined by CEMS and these are included in total emissions reported, then note this in EAOR. Add notes explaining unusual activity!

## Slide 17: Emissions Calculations Tips
  When reporting PM, PM10, and PM2.5 emissions, make sure to use the correct emission factor (EF) for the pollutant.
  Depending on the SCC and control equipment configuration, there may be EFs for primary PM, primary PM10, primary PM2.5, filterable PM, filterable PM10, filterable PM2.5 and condensable PM (CPM).
    PM filterable >= PM10 filterable >= PM2.5 filterable
    PM10 primary >= PM2.5 primary >= CPM
    NOTE: ‘primary PM’ is not reported. Rather, PM determined by standard EPA Method 5 is filterable PM, which is reported.
  The EFs listed as primary include both the filterable and condensable components. For example, primary PM2.5 is the total of PM2.5 filterable plus CPM, and primary PM10 is the total of PM10 filterable plus CPM.
    PM2.5 primary = PM2.5 filterable + CPM
    PM10 primary = PM10 filterable + CPM
  You should never add the EFs for primary and filterable together, since primary already includes the filterable.
    If reported, report condensable PM10 and condensable PM2.5 as CPM.
    PM10 condensable = PM2.5 condensable = CPM

## Slide 18: Emissions Calculations Tips
  What if I don’t know my CPM (condensable particulate matter) emissions?
  CPM emissions must be reported if the emissions unit is subject to a numerical emission limit for CPM.
  Otherwise, CPM should be reported if information is available to estimate emissions, and such emissions are equal to or greater than 5.0 tons per year per SCC. Do not add the pollutant CPM in EAOR if you do not have emissions data to report.
  A Calculator to estimate CPM emissions based on some available CPM emissions factor information from AP-42 is provided for you at this link: https://floridadep.gov/air/permitting-compliance/content/cpm-reporting-threshold.
  Here is a link to the Annual Air Emissions Calculators (based on WebFIRE Emissions Factors) for some SCCs: https://floridadep.gov/air/permitting-compliance/content/air-emissions-estimators.

## Slide 19: Common Data Quality Issues
  A change during the reporting year in the facility’s tracking/reporting methodology resulted in underreporting of emissions (i.e. from AP42- to CEMS).
  Different emissions factors are used for reporting in different systems (TRI vs. AOR).
  Overestimating previous years emissions.
  Instances where the emissions factor or fuel usage/ process rate is off by an order of magnitude; or incorrect value was used in the formula in EAOR.
  Duplication of process rate / fuel usage: The exact same process rate was reported for different fuels burned, for example diesel and natural gas.
Notes: A change during the reporting year in the facility’s tracking/reporting methodology resulted in underreporting of emissions: In this case, the facility went from using AP-42 emissions factor to using CEMS, however programming of the CEMS to switch to calculating the mass value was only available for part of the year, and emissions for the other half of the year not picked up by CEMS were inadvertently excluded (and subsequently had to be calculated based on the fuel consumed during this time using AP-42 emissions factors);
Different emissions factors are used for reporting in different systems (i.e. TRI vs. AOR comparison): AOR reporting schedule may precede TRI reporting, and in some cases, the more accurate emissions factors used for TRI, which considered specific controls, were not available until after the AOR reporting deadline (or were only utilized in TRI, and not EAOR) and consequently a comparison of emissions from the two systems showed a large disparity.
Observed a sig decrease in their NOx emissions in the current reporting year vs. previous year, which seemed out of proportion to process rate inc in current year (i.e. Nox CEMs, and NOX had decreased by 30%, in spite of a slight increase in the tons of coal burned). In this case, after follow-up with the facility, it was determined default CEMS values required to be used in the previous year overestimated actual Nox emissions for that year. Tip: When possible, add a note in EAOR explaining why the Nox emissions were higher in the previous year, compared to the current year.
Instances where the emissions factor or fuel usage/ process rate is off by an order of magnitude; or simply, not the right value was used in the formula in EAOR; or
The exact same process rate was reported for different fuels burned, for example diesel and natural gas.

## Slide 20: Common Data Quality Issues
  Instances where a facility uses a retired SCC code, which is no longer accepted by EPA.
  Cases where emissions were normally calculated by applying a control efficiency, however were inadvertently reported without it.
  Forgetting to convert emissions value to tons, and reporting in pounds because the conversion to tons was excluded from the formula
  Cases where HAP VOCs are not included with the VOC emissions.
  Formulas needing revision:
    Formula omits an important conversion factor (i.e. conversion of sulfur to SO2); and
    Incorrectly uses a “percentage” (i.e. 10% ash) instead of a “number” (i.e.0.1 ash fraction), resulting in emissions being over reported (for HAPS metals).
Notes:   Instances where a facility uses a retired SCC code, which is no longer accepted by EPA.
Cases where emissions were normally calculated by applying a control efficiency, however were inadvertently reported without it, resulting in over reporting of emissions.
Forgetting to convert emissions value to tons, and reporting in pounds because the conversion to tons was excluded from the formula.
Cases where HAP VOCs are not included with the VOC emissions.
Cases where the workbook setup to capture data for the AOR such as fuel usage, needed the formulas to be revised; or the formula omits a conversion factor (i.e. for conversion of sulfur to SO2), underreporting emissions by half; and spreadsheet incorrectly contains a “percentage” Format type (i.e. 10% ash) instead of a “number” Format type (i.e. 0.1 ash fraction), as a result HAPS metal emissions were over reported.

## Slide 21: EPA Resources
EPA’s WEBFIRE (contains EPA’s recommended emissions factors):
https://www.epa.gov/electronic-reporting-air-emissions/webfire
EPA’s Searchable SCC database (contains a list of most updated SCCs):
www.epa.gov/scc
Notes: EPA Web Resources

## Slide 22: Contacts
  Griffin Jones
  Griffin.W.Jones@FloridaDEP.gov
  850-717-9103
  Kris Lanh
  Kris.Lanh@FloridaDEP.gov
  850-717-9094
  Dylan Edeker
  Dylan.Edeker@FloridaDEP.gov
  850-717-9084
  EAOR HelpDesk
  EAOR@FloridaDEP.gov
  Jessica Dalton
  Jessica.Dalton@FloridaDEP.gov
  850-717-9106
  Elizabeth Walker
  Elizabeth.Walker@FloridaDEP.gov
  850-717-9008
  Amy Hilliard
  Amy.Hilliard@FloridaDEP.gov
  850-717-9025
  DARM HelpDesk
  DARM.HelpDesk@FloridaDEP.gov
  If you need assistance with issues related to the DEP Business Portal, please contact the IT Service Desk at 850-245-7555 or ServiceDesk@FloridaDEP.gov.
Notes: For assistance with submitting AORs, emissions calculations, or using eAOR contact Griffin Jones, Kris Lanh, or email the EAOR HelpDesk.
For assistance with general AOR regulatory and procedural requirements, contact Jessica Dalton.
For assistance with submitting Title V fees, contact Amy Hilliard, Elizabeth Walker, or email the DARM HelpDesk.
For assistance with creating a DEP Business Portal account or PIN requests, please contact the DEP IT Section.