## Slide 1: Large Quantity Generators and the Generator Improvement Rule

## Slide 2: Disclaimer
  The rule is very new, just published in the Federal Register on November 28, 2016. It’s effective on May 30, 2017 in Iowa, Alaska, the territories and tribal lands.
  The rule has not yet been adopted by Florida, so all references are to the Federal Rule only. It’s a base program rule, so it’s not effective until it’s adopted by Florida. Florida needs to adopt the more stringent sections, may adopt the neutral sections and doesn’t need to adopt the less stringent sections.
  This Presentation only covers the highlights of the new rule, mainly those for LQGs. It doesn’t cover everything included in the final rule. Some of the text of the new rule has been shortened or summarized. Please obtain a full copy of the rule for complete language.
  There are no pictures in this presentation yet.

## Slide 3: DEFINITIONS in 260
260.10
Acute hazardous waste – 261.31 code (H) [some F codes] or 261.33(e) [P codes].

## Slide 4: DEFINITIONS in 260 a
260.10
Central accumulation area (CAA)– any on-site area accumulating hazardous waste in units.
Notes: Preamble discussion on page 85743 and 85744

## Slide 5: DEFINITIONS in 260 b
260.10 – Generator categories clearly spelled out
Large Quantity Generator (LQG) – generating within a calendar month
  Greater than or equal to 1000 kg (2200 lbs.) of non-acute waste
  Greater than 1 kg (2.2 lbs.) of acute waste [261.31 or 261.33(e)]
  Greater than 100 kg (220 lbs.) of any contaminated soil, water, or debris from a from a spill of acute waste

## Slide 6: Definitions in 262
262.1
Condition for Exemption – a requirement to obtain an exemption… for example accumulating waste for longer than 90 days.
Independent Requirements – a requirement without relation to a conditional exemption… for example the pre-transport waste packaging requirements of 262.30.
Notes: See notes in the preamble on page 85746
Clarification:
In this final rule, EPA outlines in regulatory language the distinction between independent requirements for all generators and conditions for exemption from the storage facility regulations for generators who are accumulating hazardous waste on site.
  This distinction has always existed in RCRA and it has been the Agency’s position that generators not complying with a condition of a generator exemption would be considered an operator of a non-exempt storage facility.
  State regulatory agencies will continue to retain discretion and authority regarding bringing enforcement actions when non-compliance with conditions for exemptions have been detected.
  EPA and states have always had, and continue to have, enforcement discretion to bring charges and seek penalties that accurately reflect the seriousness of the violations and their potential for harm.

## Slide 7: Independent Requirements in 262
262.10 (a) – Independent Requirements are spelled out
  262.10 (a)(1) –Independent Requirements
    262.10 (a)(1)(iii) – Independent requirements of a LQG
262.10(g)(1) – A generator’s violation of an independent requirement is subject to penalty and injunction relief under section 3008 of RCRA.

## Slide 8: Conditions for Exemption in 262
262.10 (a) –Conditions for Exemption are spelled out
  262.10 (a)(2) –Conditions for Exemption
    262.10 (a)(2)(iii) – LQG that meets the condition for exemption in 262.15 and 262.17
262.10(g)(2) – A generator’s noncompliance with a condition for exemption is not subject to penalty, but noncompliance with an applicable condition for exemption is a storage facility operating without exemption from the permit, interim status and operations requirements.

## Slide 9: Determining Generator Category 262.10
262.10(b) – Determining generator category. A generator must use 262.13 to determine which provisions of this part are applicable to the generator based on the quantity of hazardous waste generated per calendar month. (New)

## Slide 10: HW Determination and Record Keeping 262.11 a
A person who generates solid waste must make a determination if it is HW to ensure wastes are managed properly – Initial steps are spelled out:
262.11(a) – The hazardous waste determination must be made at point of waste generation.
262.11(b) – Must determine if solid waste is excluded from regulation under 261.4.
262.11(c) – If solid waste is not excluded, the person must use knowledge to determine waste status.
262.11(d) – Must also determine if waste exhibits one or more hazardous characteristics.

## Slide 11: HW Determination and Record Keeping 262.11 b
If the waste is hazardous, then the generator is referred to other possible exclusions or restrictions:
262.11(e) – If the waste is determined to be hazardous, the generator must refer to parts 261, 264, 265, 266, 267, 268, and 273 for other possible exclusions or restrictions pertaining to management of the specific waste.

## Slide 12: HW Determination and Record Keeping 262.11 c
Recordkeeping requirements (New)
262.11(f) – Recordkeeping for SQGs and LQGs. Records supporting hazardous waste determinations are required. Records also need to be kept for three years.
262.11(g) – Identifying hazardous waste numbers (waste codes) is required for SQGs and LQGs.

## Slide 13: Generator Category determination 262.13
A generator must determine its generator category. A generator’s category is based on the amount of hazardous waste generated each month and may change from month to month.

## Slide 14: Table 1 to § 262.13—Generator Categories Based on Quantity of Waste Generated in a Calendar Month
Quantity of acute hazardous waste generated in a calendar month | Quantity of non-acute hazardous waste generated in a calendar month | Quantity of residues from a cleanup of acute hazardous waste generated in a calendar month | Generator category
> 1 kg | Any amount | Any amount | Large quantity generator.
Any amount | ≥ 1,000 kg | Any amount | Large quantity generator.
Any amount | Any amount | > 100 kg | Large quantity generator.
≤ 1 kg | > 100 kg and < 1,000 kg | ≤ 100 kg | Small quantity generator.
≤ 1 kg | ≤ 100 kg | ≤ 100 kg | Very small quantity generator.

## Slide 15: Satellite Accumulation Areas (SAAs) 262.15
The satellite container requirements were strengthened.
262.15(a) – A generator may accumulate as much as 55 gallons of non-acute HW or one quart of acute waste or 1 kilogram of solid acute waste.
  At or near the point of generation
  Under the control of the operator
Notes: Discussion of SAAs in preamble starting on page 85757
Note: EPA says container packaging for acute waste does not need to be included when calculating max accumulation volume of acute waste in a SAA.
SAA Clarifications:
Require that hazardous wastes not be mixed or placed in a container with other hazardous wastes that are incompatible.
Allow containers to remain open temporarily under limited circumstances, when necessary for safe operations.
Provided maximum weight in addition to volume for acute hazardous waste limit.
Clarified that “three days” means three consecutive calendar days.
Rescinded memo allowing reactive hazardous waste to be stored away from the point of generation.
Made marking and labeling requirements consistent with central accumulation areas.

## Slide 16: SAAs 262.15
These are Conditions for Exemption requirements:.
262.15(a)(1) – If a container holding HW is not in good condition or leaking, the generator must transfer the HW to a new container.
262.15(a)(2) – The generator must use a container made of or lined with a material that will not react and are compatible with the HW to be accumulated.

## Slide 17: SAAs 262.15 a
262.15(a)(3) – Special standards for incompatible wastes [(i), (ii) and (iii)].
262.15(a)(4) – A container holding hazardous waste must be closed at all times during accumulation [(i) and (ii)].
262.15(a)(5) – A generator must mark or label its container with
  (i) The words “Hazardous Waste”
  (ii) Indication of hazards (for example - characteristic codes, DOT marking, OSHA hazard statement or pictogram, NFPA label)

## Slide 18: SAAs 262.15 b
262.15(a)(6) – A generator who accumulates acute waste or non-acute hazardous waste in excess of 55-gallons non-acute or one quart or 1 kilogram of acute:
  (i) Comply within three consecutive calendar days with CAA regs found in 262.17(a).
  (ii) remove the excess to either a CAA, an on-site TSD or an off-site designated facility.
  (iii) comply during three day period and date excess.

## Slide 19: SAAs 262.15 c
262.15(a)(8) - All satellite accumulation areas operated by a LQG must meet the Preparedness, Prevention, and Emergency Procedures in Subpart M.
Note: This is new and LQGs may not currently meet all of these requirements. Subpart M will be discussed in more detail later.
Notes: Refer to page 85766. the specific changes were not included in the proposed rule.

## Slide 20: Conditions for Exemption for a LQG that Accumulates Haz Waste 262.17
A LQG my accumulate hazardous waste on site without a permit or interim status if all conditions are met.
262.17(a) Accumulation. A LQG accumulates hazardous waste on site for no more than 90 days
  262.17(a)(1) – Accumulation of HW in containers
    262.17(a)(1)(i) – Air emission standards – applicable requirements of 265 AA, BB and CC.

## Slide 21: LQG Containers 262.17
  262.17(a)(1)(ii) – Condition of containers
    Good condition.
    If it leaks, transfer waste to another container.
  262.17 (a)(1)(iii) – Compatibility of waste with container.
    Made of or lined with materials that will not react with waste.

## Slide 22: LQG Containers 262.17
262.17 (a)(1)(iv) – Management of containers
  (A) Closed
  (B) Not be opened, handled or stored in a manner that may rupture the container or cause it to leak
262.17 (a)(1)(v) – Inspection of central accumulation areas at least weekly
  Look for leaking containers or deterioration of containers
  Note: Florida has other requirements for weekly inspections.

## Slide 23: LQG Containers 262.17 a
262.17 (a)(1)(vi) – Special conditions for accumulation of ignitable and reactive wastes.
  (A) – Containers holding ignitable or reactive wastes must be located at least 50 ft. from facility’s property line. Note: new language about requesting a waiver for this.
  (B) – Special precautions to prevent accidental ignition or reaction of ignitable or reactive waste. “No Smoking” signs must be conspicuously placed.

## Slide 24: LQG Containers 262.17 b
262.17 (a)(1)(vii) – Special conditions for accumulation of incompatible wastes.
  (A) – Incompatible wastes must not be placed in same container
  (B) – HW must not be placed in an unwashed container
  (C) – Containers holding HW must be separated from incompatible wastes

## Slide 25: LQG Tanks/Drip Pads/Containment Buildings 262.17
262.17 (a)(2) – Accumulation of HW in tanks
262.17 (a)(3) – Accumulation of HW on drip pads
262.17 (a)(4) – Accumulation of HW in containment buildings

## Slide 26: LQG Containers 262.17 c
262.17 (a)(5)(i) – Labeling and Marking of Containers
  (A) Words “Hazardous Waste”.
  (B) Indication of hazards of the contents (for example - characteristic codes, DOT marking, OSHA hazard statement or pictogram, NFPA label). (New)
  (C) Accumulation start date.
Notes: Note: if containers are reused that already have appropriate markings on them it is acceptable to EPA.

## Slide 27: LQG Tanks 262.17
262.17 (a)(5)(ii) – Labeling and Marking of Tanks
  (A) Words “Hazardous Waste”.
  (B) Indication of hazards of the contents (for example - characteristic codes, DOT marking, OSHA hazard statement or pictogram, NFPA label). (New)
  (C) Inventory logs or other records to demonstrate < 90 days.
  (D) Keep records.

## Slide 28: LQG Emergency Procedures 262.17
262.17 (a)(6) - Emergency Procedures - LQGs need to comply with Subpart M of 262.

## Slide 29: 262 Subpart M-Preparedness, Prevention and Emergency Procedures for LQGs
262.250 - Applicability
  The regulation of this subpart apply to those areas of a LQG where hazardous waste is generated or accumulated on site.
  Note: This means CAAs and SAAs. This is new for SAAs.

## Slide 30: 262.251 Maintenance and Operation of Facility
262.251 - Maintenance and operation of facility
  A LQG must maintain and operate its facility to minimize the possibility of a fire, explosion, or any unplanned sudden or non-sudden release of hazardous waste or hazardous waste constituents to air, soil, or surface water which could threaten human health or the environment.

## Slide 31: 262.252 Required Equipment
262.252 - All areas deemed applicable for generation or accumulation must be equipped with the following (unless waste wouldn’t require a particular kind of equipment):
  (a)-An internal communications or alarm system capable of providing immediate instruction to personnel.
  (b)- A device such as a telephone or a hand held two way radio, capable of summoning emergency assistance.
  (c)-Portable fire extinguishers, fire control equipment, spill control equipment, and decontamination equipment.
  (d)-Water at adequate volume and pressure to supply water hose streams, sprinklers, water spray system, or foam producing equipment.
Notes: Preamble has good discussion on this starting on page 85790
EPA seems to think cell phones help, but are not enough

## Slide 32: 262.253 Testing and Maintenance of Equipment
262.253 - Testing and maintenance of equipment
  All communication, alarm system, fire, spill and decontamination equipment must be tested a maintained as necessary to assure its proper operation in time of emergency.

## Slide 33: 262.254 Access to Communications or Alarm System
262.254 - Access to communication or alarm system
  (a)- When dealing with hazardous waste all personnel should have access to alarm system and communication.
  (b)-In a case of only one employee working, that employee must have immediate access to emergency communication equipment.

## Slide 34: 262.255 Aisle Space
262.255 - Required aisle space
  A LQG must maintain aisle space to allow the unobstructed movement of personnel, fire protection equipment, spill control equipment, and decontamination equipment to any area of facility operation in an emergency, unless aisle space is not needed for these purposes.
  Florida aisle space requirements – 62-730.160(6) – Generators shall maintain adequate aisle space between containers of HW to allow for inspection of the condition and labels of the individual containers.

## Slide 35: 262.256 Arrangements with Local Authorities
262.256(a) – A LQG must attempt to make arrangements with local emergency services
  (1)- A LQG making arrangements must determine the potential need for emergency services.
  (2)- The LQG shall attempt to familiarize the emergency services with the layout of the facility, properties of HW handled, places where personnel work and other required information.
  (3)- Designate a primary emergency authority if necessary.

## Slide 36: 262.256 Arrangements with Local Authorities
262.256(b) - Maintain records documenting the arrangements or the attempt of arrangements with local authorities.
262.256(c) - A facility possessing 24-hour response capabilities may seek a waiver from the authority having jurisdiction (AHJ).

## Slide 37: 262.260 Purpose and Implementation of Contingency Plan
262.20(a) – A LQG must have a Contingency Plan for the facility. The plan must be designed to minimize hazards to human health or the environment from fires, explosions, or any unplanned sudden or non-sudden release of hazardous waste or hazardous waste constituents to air, soil or surface water.
262.20(b) – The provisions of the Plan must be carried out immediately whenever there is a fire, explosion, or release of hazardous waste or hazardous waste constituents which could threaten human health or the environment.

## Slide 38: 262.261 Content of Contingency Plan
262.261
  (a) – Description of the actions facility personnel must take in response to fire, explosion, or unplanned release of HW or HW constituents to air, soil or surface water.
  (b) – If a generator already has a Spill Prevention, Control, and Countermeasures plan, it need only amend that plan to incorporate hazardous waste management provisions.

## Slide 39: 262.261 Content of Contingency Plan a
262.261
  (c) – The Plan must describe arrangements agreed to with the local authorities.
  (d) – An updated list of names and telephone numbers of persons qualified to act as emergency coordinator. Note: addresses are not required.(New)
  (e) – A list of all emergency equipment at the facility.
  (f) – Evacuation plan for generator personnel.

## Slide 40: 262.262(a) Copies of Contingency Plan
262.262(a) - Copies of Contingency Plan and all revisions to the plan must be maintained at the LQG and the LQG must:
  (a) – Submit a copy to local emergency services and maintain a copy on site.

## Slide 41: 262.262(b) Contingency Plan Quick Reference Guide
262.262(b) - (Note: new requirement.)
  (b) – A LQG that first becomes subject to these provisions after May 30, 2017 or amending a Contingency Plan at that time must submit a quick reference guide to the local emergency responders. This guide must include:
    (1) – Types/names of hazardous waste and associated hazards.
    (2) – Estimated max amount of each hazardous waste that may be present at one time.

## Slide 42: 262.262(b) Contingency Plan Quick Reference Guide
    (3) – The identification of any hazardous wastes where exposure would require unique or special treatment by medical or hospital staff.
    (4) – A map of the facility showing where hazardous wastes are generated, accumulated, and treated and routes to these areas.
    (5) – A street map of the facility in relation to surrounding businesses, schools, and residential areas.

## Slide 43: 262.262(b) Contingency Plan Quick Reference Guide
    (6) – The locations of water supply (fire hydrant).
    (7) – The identification of on-site notifications systems.
    (8) – The names and numbers of emergency coordinators.

## Slide 44: 262.262(c) Contingency Plan Quick Reference Guide
  262.262(c) – LQGs must update as necessary the Quick Reference Guide whenever the Contingency Plan is amended and submit both documents to the local authorities.

## Slide 45: 262.263 Amendment of Contingency Plan
  262.263 – The Contingency Plan must be reviewed, and immediately amended, if necessary, whenever:
    (a) – Applicable regulations are revised.
    (b) – The Plan fails in an emergency.
    (c) – The facility changes in a way that materially increases the potential for fires, explosions or releases of HW or HW constituents or changes the response necessary in an emergency.

## Slide 46: 262.264 Emergency Coordinator
  262.264 – Emergency Coordinator (EC) requirements - At all times, there must be at least one employee either on the generator’s premises or on call with the responsibility for coordinating all emergency response measures and implementing the necessary emergency procedures.

## Slide 47: 262.265 Emergency Procedures
  262.265
  (a) – Whenever there is an imminent or actual emergency, the EC must perform certain actions:
    (1) – Activate alarms.
    (2) – Notify authorities.
  (b) – ID the character, exact source amount and areal extent of any released materials.
  (c) – Assess hazards.

## Slide 48: 262.265 Emergency Procedures
(d)(2) – The coordinator must immediately notify the government official designated or the National Response Center (800/424-8802 toll free) the following:
  (i) – Name and phone number of reporter.
  (ii) – Name and address of generator.
  (iii) – Time and type of incident.
  (iv) – Name and quantity of materials released.
  (v) – The extent of injuries, if any.
  (vi) – The possible hazards to human or environmental health outside of the facility.

## Slide 49: 262.265 Emergency Procedures a
(e) – During the emergency incident the coordinator must take reasonable measures to insure that other hazardous waste generators are not affected.
(f) – If the generator stops operations in response to an incident, the coordinator must monitor for leaks, pressure buildup, gas generation, or ruptures in valves, pipes or other equipment when appropriate
(g) – Immediately after an emergency the coordinator must provide for treating, storing, or disposing of recovered waste.

## Slide 50: 262.265 Emergency Procedures b
(h) – The emergency coordinator must ensure that the affected area(s) of the facility:
  (h)(1) – No hazardous waste that may be incompatible with the released material is treated, stored, or disposed of until clean up procedures are complete.
  (h)(2) – All emergency equipment listed in the Contingency Plan is cleaned and fit for its intended use before operations are resumed.

## Slide 51: LQGs 262.17 Personnel Training
262.17 (a)(7) - Personnel Training
  (i)
    (A) – Personnel must be trained either in the classroom, on the job, or online. (New)
    (B) – Program must be directed by a trained person.
    (C) – Training must cover certain areas.
      (1) - Inspection procedures.
      (2) – Cut-off systems.
      (3) - Alarm systems.
      (4) – Fire or explosion response.
      (5) – Groundwater contamination response.
      (6) – Shutdown of operations.
    (D) – If OSHA emergency response training has been provided, it may cover some of these requirements.
Notes: Online training is now an option.

## Slide 52: LQGs 262.17 Personnel Training a
262.17 (a)(7) - Personnel Training
  (ii) – Training within six months.
  (iii) – Annual review of initial training.
  (iv) – LQG must maintain the following documents:
    (A) – Job title.
    (B) – Job description.
    (C) – Description of training.
    (D) – Training records.
  (v) – Requirements for record retention.

## Slide 53: LQGs 262.17 Closure
262.17 (a)(8) – Closure. Prior to closing a unit or closing a facility, conditions must be followed. Units include containers, tanks, drip pads and containment buildings.
Note: The language has been changed to include containers.(New)

## Slide 54: LQGs 262.17 Closure a
  262.17 (a)(8)(i) – Notification for closure of waste accumulation unit. LQGs must perform one of the following:
    (A) – Place a notice in the operating record within 30 days after closure identifying the location of the unit.
    (B) – Meet closure performance standards.

## Slide 55: LQGs 262.17 Closure b
262.17 (a)(8)(ii) – Notification for closure of the facility:
  (A) – Notify EPA no later than 30 days prior to closing the facility.
  (B) – Notify EPA within 90 days after closing the facility.
  (C) – LQGs may request additional time.

## Slide 56: LQGs 262.17 Closure c
262.17 (a)(8)(iii) – Closure performance standards.
  262.17 (a)(8)(iii)(A) – The LQG must close in a way that:
    (1) – Minimizes the need for further maintenance.
    (2) – Removes all contaminated equipment, structures, and soil.
    (3) – Any hazardous waste generated during closing process must be managed properly.
    (4) – If any contaminated soils and wastes cannot be removed or decontaminated, then the accumulation unit is considered a landfill.

## Slide 57: LQGs 262.17 Closure d
262.17 (a)(8)(iv) – Closure performance standards for drip pads.
262.17 (a)(8)(v) – Closure performance standards do not apply to SAAs.

## Slide 58: LQGs 262.17 LDRs
262.17 (a)(9) – LQGs need to comply with applicable requirements in 268.

## Slide 59: LQGs 262.17 Accumulation Time Limit Extension
262.17 (b) – LQGs need to apply for 30 day extension if waste will be on-site for >90 days.

## Slide 60: LQGs 262.17 F006 Accumulation
262.17 (c), (d) and (e) – F006 discussion.

## Slide 61: LQGs 262.17 VSQG Waste Consolidation
262.17 (f) – LQGs may accumulate waste from VSQGs under certain conditions (under the control of the same person).(New) The LQG must:
  (1) – Notifies EPA.
    (i) – Identifies VSQGs.
    (ii) – Submits updated form when info changes.

## Slide 62: LQGs 262.17 VSQG Waste Consolidation a
  (2) – Maintains records with information required.
  (3) – Complies with applicable independent requirements and conditions for exemptions. In addition, containers or units need to be dated with the date accumulation begins (i.e. the date the HW was received).

## Slide 63: LQGs 262.17 VSQG Waste Consolidation b
260.10(1) – Definition of “person”:
An individual, trust, firm, joint stock company, Federal Agency, corporation (including a government corporation), partnership, association, State, municipality, commission, political subdivision of a State, or any interstate body.
Notes: Discussion of this in preamble on page 85807

## Slide 64: LQGs 262.17 VSQG Waste Consolidation c
VSQG requirements when shipping to a LQG:
262.14(a)(5)(viii) (A) – The VSQG and LQG must be under the control of the same “Person” as defined in 260.10. “Control” is the power to direct the policies of the generator, whether by the ownership of stock, voting rights, or otherwise. (Contractors who operate generator facilities on behalf of a different “Person” as defined in 260.10 shall not be deemed to “control” such generator.)
Notes: Discussion of this in preamble on page 85810

## Slide 65: LQGs 262.17 VSQG Waste Consolidation d
  (B) The VSQG marks its container(s) of hazardous waste with :
    (1) The words “Hazardous Waste”
    (2) ) Indication of hazards of the contents (for example - characteristic codes, DOT marking, OSHA hazard statement or pictogram, NFPA label).
Notes: Discussion of this in preamble on page 85810

## Slide 66: LQGs 262.17 Rejected Loads
262.17 (g) – LQGs Requirements for rejected loads:
  (1) – Sign Item 18c or
  (2) – Sign Item 20

## Slide 67: EPA ID Numbers and Re-notification 262.18
262.18(a) – LQGs must have an ID number.
(b) – Use Form 8700-12.
(c) – Do not use Transporters or TSDs that do not have ID numbers.
(d)(2) – A LQG must renotify EPA by March 1st of each even numbered year thereafter. This can be submitted as part of the BR.
(e) – Imports or exports.

## Slide 68: LQG Marking 262.32
262.32(b) – A generator must mark hazardous waste containers of 119 gallons or less before transportation:
  (1) – HAZARDOUS WASTE–Federal Law Prohibits Improper Disposal. If found, contact the nearest police or public safety authority or the U.S. Environmental Protection Agency.
  (2) – Generator’s Name and Address.
  (3) – Generator’s EPA ID Number.
  (4) – Manifest Tracking Number.
  (5) – EPA Hazardous Waste number(s) (New)

## Slide 69: LQG Marking 262.32 a
262.32(c) – A generator may us a nationally recognized electronic system, such as barcoding to identify EPA hazardous waste number(s). (New)
262.32(d) – Lab packs that will be incinerated in compliance with 268.42 are not required to be marked with EPA hazardous waste numbers, except D004, D005, D006, D007, D008, D010 and D011 where applicable.(New)

## Slide 70: 262.35 Liquids in Landfills Prohibition
262.35 - The placement of bulk or non-containerized liquid hazardous waste or hazardous waste containing free liquids in any landfill is prohibited.

## Slide 71: 262 Subpart D Recordkeeping
Recordkeeping and reporting applicable to LQGs
262.40 Recordkeeping
  (c) – See 262.11(f) for recordkeeping requirements for documenting hazardous waste determinations.

## Slide 72: 262.41 Biennial Report for LQGs
262.41(a) – A LQG for at least one month of a odd- numbered year that ships any hazardous waste must complete and submit EPA Form 8700-13 A/B by March 1 of the next even-numbered year.
262.41(b) – A LQG for at least one month of a odd-numbered year who treats, stores, or disposes of hazardous waste on-site must complete and submit EPA Form 8700-13 A/B by March 1 of the next even-numbered year. This also applies to LQGs that receive waste from VSQGs.
262.41(c) Exports of hazardous waste to foreign countries are not required to be reported on Biennial Reports. Exporters use a separate form.
Notes: Final Rule: Biennial Report (BR) Clarifications Consistent with Existing BR Guidance
  Regulations will not list specific data elements to be reported, but instead refer generators directly to the form instructions
LQGs must report all hazardous waste generated in a calendar year, even when it is managed the next calendar year
LQGs must report hazardous wastes generated throughout the calendar year, even for months when they are an SQG
Closing Regulatory Gap
Recycling facilities that do not have a RCRA permit because they don’t store must report wastes being recycled

## Slide 73: 268.7 LDRs
268.7 - Testing, tracking, and recordkeeping requirements for generators, treaters, and disposal facilities
  (a)(5) – If a generator is managing and treating prohibited wastes or contaminated soil in tanks, containers, or containment building must develop and follow a written waste analysis plan that must be kept on site in the generators records

## Slide 74: Stringency of Final Rule
More stringent:
  SQG re-notification.
  Identifying hazards of wastes being accumulated and labeling.
  Notification of closure.
  Closure as a landfill for LQGs accumulating hazardous wastes in containers that cannot meet closure performance standards.
  Biennial reporting for whole year, not just months the generator was an LQG.
  Biennial reporting for recyclers who don’t store prior to recycling.
  Quick Reference Guide for Contingency Plans.
Notes: This slide is from EPA RIN presentation.
Also see preamble page 85801

## Slide 75: Stringency of Final Rule a
Less stringent:
  VSQG consolidation.
  Episodic generation.
  Waiver from 50-foot rule.
Notes: This slide is from EPA RIN presentation.

## Slide 76: Major Impacts of Final Rule by Generator Category
New Provision | VSQG | SQG | LQG
LQG Consolidation of VSQG wastes | X |  | X
Episodic Generation | X | X | 
50-foot Waiver |  |  | X
Marking & Labeling |  | X | X
Marking RCRA Waste Codes |  | X | X
SQG Re-notification |  | X | 
Contingency Plan Quick Reference Guide |  |  | X
Closure Notification |  |  | X
Closure as Landfill if Can’t Clean Close |  |  | X
BR Reporting by Recyclers Who Don’t Store* |  | X | X

## Slide 77: Table 5—Crosswalk of Previous Citations to New Citations for LQGs
Regulation | Previous citation | New citation | Comment
Definition of Large Quantity Generator | N/A | § 260.10 | New definition.
Accumulation Time Limit | § 262.34(a) | § 262.17(a) | Moved from § 262.34.
Accumulation in Containers | § 262.34(a)(1)(i) references part 265 subparts I, AA, BB, and CC | § 262.17(a)(1) (§ 262.17(a)(1) also references part 265 subparts AA, BB, CC) | There is still a cross-reference to part 265 subparts AA, BB, and CC because of the length of these regulations.
Accumulation in Tanks | § 262.34(a)(1)(ii) references part 265 subparts J, AA, BB, and CC | § 262.17(a)(2) references part 265 subparts J, AA, BB, CC | There is still a cross- reference to part 265 subparts J, AA, BB, CC because of the length of these regulations.
Accumulation on Drip Pads | § 262.34(a)(1)(iii) (§ 262.34(a)(1)(iii) also references part 265 subpart W) | § 262.17(a)(3) (§ 262.17(a)(3) also references part 265 subpart W) | Accumulation time limit and recordkeeping provisions move to § 262.17 and the extensive technical standards remain in part 265.
Accumulation in Containment Buildings | § 262.34(a)(1)(iv) (§ 262.34(a)(1)(iv) also references part 265 subpart DD) | § 262.17(a)(4) (§ 262.17(a)(4) also references part 265 subpart DD) | Accumulation time limit, labeling, and recordkeeping provisions move to § 262.17 and the extensive technical standards remain in part 265.
Marking and Labeling | § 262.34(a)(2) and (3) | § 262.17(a)(5) | Moved from § 262.34.
Preparedness, Prevention, and Emergency Procedures | § 262.34(a)(4) references part 265 subparts C and D | § 262.17(a)(6) references part 262 subpart M | Cross-references remain but to a new subpart of the generator regulations.
Personnel Training | § 262.34(a)(4) | § 262.17(a)(7) | Moved from § 262.34.
Closure | § 262.34(a)(1)(iv)B) references §§ 265.11 and 265.114. Section 265.111 references other sections in part 265 | § 262.17(a)(8) | Duplicated from §§ 265.11 and 114 with some revisions.
Land Disposal Restrictions | § 262.34(a)(4) references applicable parts of part 268 | § 262.17(a)(9) | There is still a cross-reference to part 268.
Extension of Accumulation Times | § 262.34(b) | § 262.17(b) | Moved from § 262.34.
Accumulation of F006 | § 262.34(g) through (i) | § 262.17(c) through (e) | Moved from § 262.34.
Accepting waste from VSQGs under the control of the same person to consolidate before sending to TSDF | N/A | § 262.17(f) | New provision.
Rejected Loads | § 262.34(m) | § 262.17(g) | Moved from § 262.34.

## Slide 78: Questions ?
Hazardous Waste Program
8800 Baymeadows Way West
Suite 100 Jacksonville, Florida 32256 (904) 256-1700 (904) 256-1588 fax