## Slide 1: Universal Waste – SQH Requirements

## Slide 2: Universal Waste 1
Standards for Universal Waste Management
40 CFR 273.2-5

## Slide 3: Universal Waste 2
40 CFR Part 273
  Waste Batteries (40 CFR 273.2)
  Waste Pesticides - “Suspended and Recalled Pesticides” (40 CFR 273.3)
  Waste Mercury-Containing Devices (40 CFR 273.4)
  Waste Mercury-Containing Lamps (40 CFR 273.5)
Rule 62-730.186, F.A.C.
  Waste Pharmaceuticals (Universal Pharmaceutical Waste rule)
Rule 62-737, F.A.C.
  Spent mercury-containing lamps and devices
Notes: Each category has slightly different requirements

## Slide 4: Universal Waste (UW) Handlers
Small Quantity Handler (SQHs) [40 CFR 273 Subpart B]
  Does not accumulate 5,000 kilograms or more of universal waste (batteries, pesticides, mercury-containing equipment, or lamps) at any time
  Not required to notify DEP or obtain an EPA ID number
Large Quantity Handlers (LQHs) [40 CFR 273 Subpart C]
  Accumulates 5,000 kilograms or more of total universal waste (batteries, pesticides, mercury-containing equipment, or lamps) at any time
  Designation is retained through the end of the calendar year
  Required to notify DEP and obtain an EPA ID number
Note: If managed as UW, waste does not count towards HW generator status

## Slide 5: Definitions and Basics
Batteries
  Spent lead acid not managed under 40 CFR 266 subpart G
  Hazardous waste batteries (those that exhibit a characteristic)
Mercury-Containing Devices
  Device or part of a device that contains elemental mercury integral to its function
  Excludes waste that is non-hazardous
  Excludes equipment or devices where mercury-containing components have been removed (specific regulations cover removal)
Mercury-Containing Lamps
  Bulb or tube portion of an electric lighting device
  Excludes lamps that are not yet waste
  Lamps that are not hazardous waste

## Slide 6: Examples of Universal Waste -Batteries

## Slide 7: Examples of Universal Waste – Mercury-Containing Equipment

## Slide 8: Examples of Universal Waste – Mercury-Containing Lamps
Notes: Green tips do contain mercury!

## Slide 9: Prohibitions
40 CFR 273.11
SQHs of universal waste may not
  Dispose of the universal waste (cannot throw in solid waste trash or other means of disposal)
  Treat or dilute universal waste, except by responding to a release

## Slide 10: Notification
SQHs are not required to notify EPA of universal waste handling activities
  40 CFR 273.12

## Slide 11: Management
Battery Management (SQH)
  40 CFR 273.13 (a) – Must be managed in a way to prevent release
    Contain batteries that show signs of leakage
      Container must be closed, sealed, and structurally sound
      Compatible with the battery type and lack evidence of spillage or leakage
    May conduct the following activities as long as each individual battery cell remains intact and closed:
      Sort batteries by type
      Properly discharge batteries
      Regenerate used batteries
      Properly remove and manage electrolyte (additional regulations apply)
Notes: SQHs are not exempt from USDOT standards regarding battery shipments

## Slide 12: Improper Management 1
Notes: They should not be comingled with other waste and other types of batteries.

## Slide 13: Improper Management 2
Notes: This container had fallen over AFTER the pallet had rotted and they didn’t attempt to clean-up the UW spill.

## Slide 14: Proper Management

## Slide 15: Management 1
Mercury-Containing Equipment Management
  40 CFR 273.13(c) – Must be managed in a way to prevent release
    Contain equipment that shows evidence of leakage
      Container must be closed, sealed, and structurally sound
      Compatible with the equipment type and lack evidence of spillage or leakage
      Must be reasonable capable of preventing release of mercury by any means
    May conduct the following activities as long as mercury is not allowed to escape:
      Remove and manage ampules
        They are removed and managed in a proper manner
        They are removed over or in a containment device
        There is a mercury clean-up system in place
        Spills are managed properly
        It is ensured the area is well ventilated and monitored
        Proper employee training is ensured
        Removed ampules are stored in proper containers with adequate packing material
        A hazardous waste determination will be performed on clean-up waste or equipment and then properly managed based upon the determination
      Remove mercury from original housing (additional regulations apply)

## Slide 16: Improper Management 3
Notes: Open containers and broken mercury thermometers. Also, note the thermostat mixed in with the batteries. This one has mercury ampules in it.

## Slide 17: Proper Management 1
Notes: Closed, properly labeled and dated container.

## Slide 18: Management 2
Mercury Containing Lamps Management
  40 CFR 273.13(d) – Must be managed in a way to prevent release
    Contain ANY lamp (leaking or non-leaking)
      Container must be closed, sealed, and structurally sound to prevent breakage
      Compatible with the lamp type and lack evidence of spillage or leakage
      Must be reasonable capable of preventing release of mercury by any means
      Must immediately clean up and place into a container any lamp that is broken or shows signs of leakage

## Slide 19: Improper Management 4
Notes: Bulbs not in a container, a broken bulb in a paper towel, and a broken bulb on a cart are examples of improper management.

## Slide 20: Improper Management 5
Notes: Bulbs not in a container, broken bulbs on the ground are examples of improper management.

## Slide 21: Improper Management 6
Notes: Bulbs not in closed, properly labeled and dated containers.

## Slide 22: Proper Management 2
Notes: Closed, properly labeled and dated containers.
The facility may want to store these on their sides, however, because they could fall over and the lamps inside may break.

## Slide 23: Labeling 1
Batteries
  SQHs – 40 CFR 273.14(a)
    “Universal Waste–Battery(ies)”
    “Waste Battery(ies)”
    “Used Battery(ies)”
Mercury-Containing Equipment
  SQHs – 40 CFR 273.14(d)
    “Universal Waste–Mercury-Containing Equipment”
    “Waste Mercury-Containing Equipment”
    “Used Mercury-Containing Equipment”
    If container contains ONLY thermostats, may replace “Mercury-Containing Equipment” with the word “Thermostats”
Mercury-Containing Lamps
  SQHs – 40 CFR 273.14(e)
    “Universal Waste Mercury-Containing Lamps”
    “Waste Mercury-Containing Lamps”
    “Used Mercury-Containing Lamps”

## Slide 24: Labeling 2
Notes: Closed, properly labeled and dated containers.

## Slide 25: Accumulation Time Limit 1
SQHs may accumulate universal waste for no longer than one year [40 CFR 273.15 (a - c)]
  May accumulate longer IF accumulation is solely for the purposes of accumulation of such quantities necessary to facilitate proper recovery, treatment, or disposal (handler bears burden of proof)
  Must be able to demonstrate length of accumulation time
    Marking or labeling container
    Marking or labeling each individual item
    Maintaining an inventory system
    Marking the accumulation area
    Any other method which clearly demonstrates the length of accumulation

## Slide 26: Accumulation Time Limit 2
Notes: This waste had been accumulating for longer than one year.

## Slide 27: Personnel Training 1
  SQHs - All employees that handle UW should be trained in the proper handling and emergency procedures appropriate to the type of UW at the facility
  40 CFR 273.16

## Slide 28: Personnel Training 2
Notes: Personnel training might be cited if employees intentionally break or dispose of spent bulbs.

## Slide 29: Response to Release
SQHs must:
  Immediately contain releases
  Perform a hazardous waste determination on residues from releases and properly manage residues
  40 CFR 273.17 (a and b)

## Slide 30: Improper Response to Release
Notes: Broken bulbs should be managed in closed, properly labeled and dated containers.

## Slide 31: Lamp Crushers
A side note…
  Lamp crushers should remain closed when not in use
  Area around crusher should be monitored for release, and all releases should be immediately responded to
Notes: Make sure bulb crusher is closed, that the filter receives proper maintenance, and that there is no broken glass on the floor around or on top of the bulb crusher. The bulb crusher should be one that is purchased. Be wary of home-made bulb crushers.
62-737.400(6), FAC – Also be reminded that we don’t allow them for anyone except the generator and a permitted destination facility. Improper maintenance may expose the employee to mercury.
Crushed lamps are still regulated, as the filter does not make the crushed lamps non-hazardous.

## Slide 32: Off-Site Shipments
SQHs must:
  Send UW only to a UW handler, destination facility, or foreign destination
  May self-transport if complying with transporter requirements in subpart D
  Comply with U.S. DOT requirements if UW is a hazardous material
  Before shipment, ensure that it will be received
Rejection of shipment
  If shipment is rejected, receive it back or ship to another destination facility
  If rejecting a shipment, contact originating handler, ship to originating handler or to another destination facility
  If shipment received is hazardous waste and not UW, notify EPA/DEP
  If shipment received is non-hazardous, but not UW, the waste may be managed appropriately
40 CFR 273.18 (a – h)

## Slide 33: Tracking Shipments
SQHs are not required to keep record of shipments
  40 CFR 273.19
Notes: However, pursuant to 40 CFR 261.2(f), you may ask a generator to show that he is managing the waste in accordance with an exclusion, and submit documentation of that.

## Slide 34: Electronic Waste
E-waste is the term used to describe end-of-life electronics
Computers and televisions are specifically targeted for recycling because of the high levels of lead found in their cathode ray tubes (CRTs)
Notes: E-waste is not included in the list of universal wastes at this time. We have chosen not to regulate e-waste demanufacturing operations as hazardous waste management facilities. However, many of these products contain universal waste lamps, mercury switches, universal waste batteries, as well as other conditionally excluded materials such as cathode ray tubes and printed circuit boards. Collectors and demanufacturers should manage these items properly.

## Slide 35: Improper Management – E-Waste
Notes: Electronic waste may be hazardous waste due to elevated levels of heavy metals. CRTs in the trash is usually cited as improper disposal of hazardous waste due to the lead content of the glass.
These items should be properly recycled.

## Slide 36: Questions ?
Hazardous Waste Program
8800 Baymeadows Way West
Suite 100 Jacksonville, Florida 32256 (904) 256-1700 (904) 256-1588 fax